## Slide 1: Prediksi Mikroorganisme pada Tambak Udang berbasis Neural Network
Advisor 1 :
Dr. Setiawardhana, S.T, M.T.
NIP. 197708242 00501 1 001
Advisor 2 :
Dr. Eng. Bima Sena Bayu Dewantara, S.ST, M.T.
NIP. 197612151 99903 1 003
Advisor 3 :
Dr. Eng. Agus Indra Gunawan, S.T, M.Sc
NIP. 197608212 00112 1 002
Muhammad Wafiq Kamaluddin (2210181042)

## Slide 2: Outline
01
02
03
04
05
06
07
Background of The Study
Purpose of The Study
Problem Formulation
Scope and Limitation
Review of Literature
System Design and Progress
Progress Detail

## Slide 3: Background of The Study
in aquaculture, especially shrimp ponds, pay attention to the environment where the cultivation is in order to obtain maximum yields. Water quality is one of the most important things to pay attention to. In fact, the most important factor in water quality is the oxygen content, which affects the pH value. Often this level is influenced by aquatic bio-organisms, especially algae. Algae monitoring can be done by looking at the color of the water. This is where the idea for the study of water quality came from. it is hoped that this tool will be able to monitor algae as in a lab test

## Slide 4: Purpose
Creating a tool to record data on samples
Create a prediction system based on recorded data

## Slide 5: Problem formulation
How to create device for data collecting
How to make good model for predict the sample

## Slide 6: Scope and Limitation
Sample is conditioned data whose concentration level is known.
Model is created from the data recorded from the device

## Slide 7: Literature review
A. I. Gunawan, B. S. B. Dewantara, A. E. Pratama, I. Puspitasari, T. A. Setya. (2019). A Study for Estimation of Bio Organism Content on Aquaculture Pond Based on Image Color and Light Intensity. International Electronics Symposium on Engineering Technology and Applications (IES-ETA). Surabaya, Indonesia, : doi:10.1109/ELECSYM.2019.8901544.
O. Meiyanto, A. I. Gunawan, dan B. S. B. Dewantara. (2021, November). Studi Analisis Konsentrasi Warna Pada Cairan Pewarna Makanan Dengan Metode Pengukuran Optical Density. Briliant, Hal. 710-725.

## Slide 8: System Design

## Slide 9: Flowchart

## Slide 10: Prototype Design

## Slide 11: Prototype

## Slide 12: Data

## Slide 13: Water

## Slide 14
Chart: Mean Histogram Value from Water in Microscope Image
Mean R Mik | 202 | 200 | 196
Mean G Mik | 208 | 207 | 201
Mean B Mik | 205 | 205 | 197
Chart: Max Histogram Value from Water in Microscope Image
Max R Mik | 206 | 206 | 200
Max G Mik | 209 | 210 | 203
Max B Mik | 209 | 210 | 199

## Slide 15
Chart: Mean Histogram Value from Water in Camera Image
Mean R Cam | 99 | 97 | 96
Mean G Cam | 93 | 94 | 93
Mean B Cam | 77 | 71 | 70
Chart: Max Histogram Value from Water in Camera Image
Max R Cam | 148 | 148 | 148
Max G Cam | 196 | 196 | 196
Max B Cam | 76 | 76 | 76
Chart: Sensor RGB Value in Water
Sensor R | 87 | 86 | 86
Sensor G | 85 | 84 | 86
Sensor B | 87 | 89 | 86

## Slide 16: Single Food Coloring

## Slide 17: Sample Composition
Concentration | Composition
0 % Food Colorant | 4 ml air
5 % Food Colorant | 0.2 ml Food Colorant + 3.8 ml water
10 % Food Colorant | 0.4 ml Food Colorant + 3.6 ml water
25 % Food Colorant | 1 ml Food Colorant + 3 ml water
50 % Food Colorant | 2 ml Food Colorant + 2 ml water
100 % Food Colorant | 4 ml Food Colorant

## Slide 18: Red

## Slide 19
Chart: Mean Histogram Value from Red Food Colorant in Microscope Image
| 0% | 5% | 10% | 25% | 50% | 100% | Pewarna Merah Pewarna Biru
Mean R Mik | 202 | 254 | 254 | 254 | 254 | 254
Mean G Mik | 202 | 108 | 131 | 130 | 140 | 137
Mean B Mik | 197 | 164 | 218 | 229 | 197 | 95
Chart: Max Histogram Value Red from Food Colorant in Microscope Image
| 0% | 5% | 10% | 25% | 50% | 100% | Pewarna Merah Pewarna Biru
Max R Mik | 201 | 255 | 255 | 255 | 255 | 255
Max G Mik | 208 | 112 | 136 | 132 | 141 | 135
Max B Mik | 203 | 173 | 233 | 228 | 200 | 98

## Slide 20
Chart: Mean Histogram Value from Red Food Colorant in Camera Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Mean R Cam | 148 | 142 | 142 | 139 | 136 | 89
Mean G Cam | 139 | 134 | 128 | 122 | 113 | 63
Mean B Cam | 114 | 111 | 104 | 102 | 97 | 44
Chart: Max Histogram Value from Red Food Colorant in Camera Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Max R Cam | 148 | 145 | 147 | 148 | 145 | 89
Max G Cam | 139 | 178 | 171 | 158 | 150 | 63
Max B Cam | 114 | 87 | 87 | 89 | 83 | 44
Chart: Sensor RGB Value from Red Food Colorant
| 0% | 5% | 10% | 25% | 50% | 100% | Pewarna Merah Pewarna Biru
Sensor R | 80 | 100 | 103 | 109 | 123 | 132
Sensor G | 92 | 74 | 72 | 63 | 50 | 44
Sensor B | 90 | 87 | 83 | 87 | 88 | 84

## Slide 21: Green

## Slide 22
Chart: Mean Histogram Value from Green Food Colorant in Microscope Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Mean R Mik | 0 | 60 | 95 | 0 | 0 | 0
Mean G Mik | 236 | 190 | 215 | 249 | 237 | 246
Mean B Mik | 252 | 100 | 129 | 111 | 81 | 65
Chart: Max Histogram Value from Green Food Colorant in Microscope Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Max R Mik | 0 | 65 | 95 | 0 | 0 | 0
Max G Mik | 245 | 187 | 218 | 255 | 245 | 248
Max B Mik | 255 | 106 | 132 | 119 | 81 | 66

## Slide 23
Chart: Mean Histogram Value from Green Food Colorant in Camera Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Mean R Cam | 63 | 117 | 118 | 81 | 62 | 51
Mean G Cam | 84 | 124 | 124 | 112 | 100 | 73
Mean B Cam | 57 | 89 | 89 | 60 | 50 | 33
Chart: Max Histogram Value from Green Food Colorant in Camera Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Max R Cam | 57 | 127 | 128 | 92 | 65 | 51
Max G Cam | 159 | 169 | 170 | 156 | 141 | 73
Max B Cam | 19 | 63 | 61 | 31 | 23 | 33
Chart: Sensor RGB Value from Green Food Colorant
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Sensor R | 38 | 64 | 88 | 69 | 61 | 64
Sensor G | 113 | 128 | 90 | 112 | 123 | 116
Sensor B | 116 | 64 | 82 | 77 | 74 | 72

## Slide 24: Blue

## Slide 25
Chart: Mean Histogram Value from Blue Food Colorant in Microscope Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Mean R Mik | 0 | 0 | 0 | 0 | 0 | 0
Mean G Mik | 231 | 237 | 181 | 157 | 127 | 242
Mean B Mik | 253 | 252 | 236 | 244 | 253 | 254
Chart: Max Histogram Value from Blue Food Colorant in Microscope Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Max R Mik | 0 | 0 | 0 | 0 | 0 | 0
Max G Mik | 233 | 255 | 204 | 161 | 127 | 243
Max B Mik | 255 | 255 | 255 | 255 | 255 | 255

## Slide 26
Chart: Mean Histogram Value from Blue Food Colorant in Camera Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Mean R Cam | 60 | 83 | 79 | 62 | 35 | 34
Mean G Cam | 82 | 106 | 107 | 97 | 78 | 54
Mean B Cam | 58 | 80 | 79 | 75 | 66 | 43
Chart: Max Histogram Value from Blue Food Colorant in Camera Image
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Max R Cam | 57 | 93 | 78 | 73 | 43 | 34
Max G Cam | 159 | 149 | 149 | 141 | 124 | 54
Max B Cam | 19 | 47 | 39 | 43 | 18 | 43
Chart: Sensor RGB Value from Blue Food Colorant
| 0 | 0.05 | 0.1 | 0.25 | 0.5 | 1
Sensor R | 37 | 51 | 53 | 36 | 21 | 19
Sensor G | 110 | 100 | 103 | 111 | 110 | 114
Sensor B | 110 | 106 | 106 | 111 | 123 | 126

## Slide 27: Double Food Coloring Mixture

## Slide 28: Sample Composition
Concentration | Composition
0 % First Colorant 100 % Second Colorant | 4 ml Second Colorant
20 % First Colorant 80 % Second Colorant | 0.8 ml First Colorant + 3.2 ml Second Colorant
40 % First Colorant 60 % Second Colorant | 1.6 ml First Colorant + 2.4 ml Second Colorant
60 % First Colorant 40 % Second Colorant | 2.4 ml First Colorant + 1.6 ml Second Colorant
80 % First Colorant 20 % Second Colorant | 3.2 ml First Colorant + 0.8 ml Second Colorant
100 % First Colorant 0 % Second Colorant | 4 ml First Colorant

## Slide 29: Red and Green

## Slide 30
Chart: Mean Histogram Value from Red and Green Mixture Food Colorant Histogram Microscope
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Mean R Mik | 0 | 22 | 92 | 163 | 254 | 254
Mean G Mik | 246 | 227 | 140 | 174 | 135 | 138
Mean B Mik | 65 | 65 | 41 | 53 | 89 | 101
Chart: Mean Histogram Value from Red and Green Mixture Food Colorant Microscope Image
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Max R Mik | 0 | 24 | 92 | 176 | 255 | 255
Max G Mik | 248 | 235 | 140 | 175 | 143 | 143
Max B Mik | 66 | 69 | 41 | 54 | 88 | 103
Mean R Mik | 0 | 22 | 92 | 163 | 254 | 254
Mean G Mik | 246 | 227 | 140 | 174 | 135 | 138
Mean B Mik | 65 | 65 | 41 | 53 | 89 | 101

## Slide 31
Chart: Mean Histogram Value from Red and Green Mixture Food Colorant Camera Image
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100%
Mean R Cam | 51 | 86 | 104 | 96 | 109 | 92
Mean G Cam | 73 | 91 | 100 | 92 | 97 | 65
Mean B Cam | 33 | 51 | 61 | 54 | 63 | 46
Chart: Max Histogram Value from Red and Green Mixture Food Colorant Camera Image
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100%
Max R Cam | 57 | 103 | 123 | 96 | 133 | 103
Max G Cam | 117 | 161 | 133 | 92 | 127 | 85
Max B Cam | 16 | 54 | 56 | 54 | 67 | 43
Chart: Sensor RGB Value from Red and Green Mixture Food Colorant
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Sensor R | 64 | 72 | 85 | 88 | 98 | 134
Sensor G | 116 | 106 | 89 | 88 | 78 | 44
Sensor B | 72 | 81 | 81 | 83 | 86 | 81

## Slide 32: Red and Blue

## Slide 33
Chart: Mean Histogram Value from Red and Blue Mixture Food Colorant Microscope Image
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Mean R Mik | 0 | 0 | 52 | 56 | 251 | 254
Mean G Mik | 228 | 227 | 140 | 174 | 135 | 138
Mean B Mik | 254 | 65 | 41 | 53 | 89 | 101
Chart: Max Histogram Value from Red and Blue Mixture Food Colorant Microscope Image
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Max R Mik | 0 | 24 | 92 | 176 | 255 | 255
Max G Mik | 229 | 235 | 140 | 175 | 143 | 143
Max B Mik | 255 | 69 | 41 | 54 | 88 | 103

## Slide 34
Chart: Mean Histogram Value from Red and Blue Mixture Food Colorant Camera Image
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100%
Mean R Cam | 66 | 86 | 104 | 96 | 109 | 92
Mean G Cam | 84 | 91 | 100 | 92 | 97 | 65
Mean B Cam | 65 | 51 | 61 | 54 | 63 | 46
Chart: Max Histogram Value from Red and Blue Mixture Food Colorant Camera Image
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100%
Max R Cam | 57 | 103 | 123 | 96 | 133 | 103
Max G Cam | 159 | 161 | 133 | 92 | 127 | 85
Max B Cam | 19 | 54 | 56 | 54 | 67 | 43
Chart: Sensor RGB Value from Red and Blue Mixture Food Colorant
| 100% 0% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Sensor R | 38 | 72 | 85 | 88 | 98 | 134
Sensor G | 108 | 106 | 89 | 88 | 78 | 44
Sensor B | 112 | 81 | 81 | 83 | 86 | 81

## Slide 35: Green and Blue

## Slide 36
Chart: Mean Histogram Value from Green and Blue Mixture Food Colorant Microscope Image
| 0% 100% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Mean R Mik | 0 | 0 | 0 | 0 | 0 | 0
Mean G Mik | 228 | 244 | 244 | 248 | 241 | 246
Mean B Mik | 254 | 164 | 106 | 146 | 100 | 65
Chart: Max Histogram Value from Green and Blue Mixture Food Colorant Microscope Image
| 0% 100% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Max R Mik | 0 | 0 | 0 | 0 | 0 | 0
Max G Mik | 229 | 250 | 251 | 255 | 255 | 248
Max B Mik | 255 | 168 | 111 | 177 | 125 | 66

## Slide 37
Chart: Mean Histogram Value from Green and Blue Mixture Food Colorant Camera Image
| 0% 100% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100%
Mean R Cam | 66 | 71 | 79 | 76 | 81 | 51
Mean G Cam | 84 | 110 | 109 | 108 | 110 | 73
Mean B Cam | 65 | 64 | 62 | 61 | 61 | 33
Chart: Max Histogram Value from Green and Blue Mixture Food Colorant Camera Image
| 0% 100% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100%
Max R Cam | 57 | 96 | 102 | 99 | 105 | 57
Max G Cam | 159 | 178 | 170 | 171 | 176 | 117
Max B Cam | 19 | 43 | 44 | 39 | 117 | 16
Chart: Sensor RGB Value from Green and Blue Mixture Food Colorant
| 0% 100% | 80% 20% | 60% 40% | 40% 60% | 20% 80% | 0% 100% | Pewarna Merah Pewarna Biru
Sensor R | 38 | 48 | 49 | 50 | 56 | 64
Sensor G | 108 | 114 | 119 | 120 | 121 | 116
Sensor B | 112 | 98 | 90 | 89 | 81 | 72

## Slide 38: Triple Food Coloring Mixture

## Slide 39: Sample Composition
Concentration | Composition
20 % Red Colorant 60 % Green Colorant 20 % Blue Colorant | 0.8 ml Red Colorant + 2.4 ml Green Colorant + 0.8 ml Blue Colorant
20 % Red Colorant 40 % Green Colorant 40 % Blue Colorant | 0.8 ml Red Colorant + 1.6 ml Green Colorant + 1.6 ml Blue Colorant
20 % Red Colorant 20 % Green Colorant 60 % Blue Colorant | 0.8 ml Red Colorant + 0.8 ml Green Colorant + 2.4 ml Blue Colorant
40 % Red Colorant 40 % Green Colorant 20 % Blue Colorant | 1.6 ml Red Colorant + 1.6 ml Green Colorant + 0.8 ml Blue Colorant
40 % Red Colorant 20 % Green Colorant 40 % Blue Colorant | 1.6 ml Red Colorant + 0.8 ml Green Colorant + 1.6 ml Blue Colorant
60 % Red Colorant 20 % Green Colorant 20 % Blue Colorant | 2.4 ml Red Colorant + 0.8 ml Green Colorant + 0.8 ml Blue Colorant
33 % Red Colorant 33 % Green Colorant 33 % Blue Colorant | 1.3 ml Red Colorant + 1.3 ml Green Colorant + 1.3 ml Blue Colorant

## Slide 40: Red (20 %) Green (20 %) and Blue(60 %)

## Slide 41
Chart: Mean Histogram Value from Red Green, and Blue Mixture Food Colorant Camera Image
Mean R Mik | 0 | 0 | 0
Mean G Mik | 153 | 148 | 152
Mean B Mik | 75 | 62 | 76
Chart: Max Histogram Value from Red Green, and Blue Mixture Food Colorant Camera Image
Max R Mik | 0 | 0 | 0
Max G Mik | 166 | 164 | 166
Max B Mik | 84 | 70 | 84
Image Result

## Slide 42
Chart: Mean Histogram Value from Red Green, and Blue Mixture Food Colorant Microscope Image
Mean R Cam | 95 | 91 | 90
Mean G Cam | 103 | 103 | 102
Mean B Cam | 62 | 61 | 61
Chart: Max Histogram Value from Red Green, and Blue Mixture Food Colorant Microscope Image
Max R Cam | 123 | 123 | 123
Max G Cam | 133 | 133 | 133
Max B Cam | 56 | 56 | 56
Chart: RGB Sensor Value from Red Green, and Blue Mixture Food Colorant
Sensor R | 75 | 76 | 75
Sensor G | 94 | 94 | 94
Sensor B | 90 | 89 | 90
Image Result

## Slide 43: Red (40 %) Green (40 %) and Blue(20 %)

## Slide 44
Chart: Mean Histogram Value from Red Green, and Blue Mixture Food Colorant Camera Image
Mean R Mik | 0 | 0 | 0
Mean G Mik | 153 | 148 | 152
Mean B Mik | 75 | 62 | 76
Chart: Max Histogram Value from Red Green, and Blue Mixture Food Colorant Camera Image
Max R Mik | 0 | 0 | 0
Max G Mik | 166 | 164 | 166
Max B Mik | 84 | 70 | 84
Image Result

## Slide 45
Chart: Mean Histogram Value from Red Green, and Blue Mixture Food Colorant Microscope Image
Mean R Cam | 95 | 91 | 90
Mean G Cam | 103 | 103 | 102
Mean B Cam | 62 | 61 | 61
Chart: Max Histogram Value from Red Green, and Blue Mixture Food Colorant Microscope Image
Max R Cam | 123 | 123 | 123
Max G Cam | 133 | 133 | 133
Max B Cam | 56 | 56 | 56
Chart: RGB Sensor Value from Red Green, and Blue Mixture Food Colorant
Sensor R | 75 | 76 | 75
Sensor G | 94 | 94 | 94
Sensor B | 90 | 89 | 90
Image Result

## Slide 46: ANN

## Slide 47: ANN Model and Result

## Slide 48: Model
No | Parameter | Value
1. | Number of neurons in the input layer | 15
2. | Number of hidden layers | 3
3. | Number of neurons in the output layer | 3
4. | Epoch | 250
5. | Learning rate | 0,0004
6. | Normalization | yes

## Slide 49: Result
No | Sample Concentration Content (%) |  |  |  |  |  |  |  | 
 | Actual |  |  | Prediction |  |  | Absolute error |  | 
 | R | G | B | R | G | B | R | G | B
1. | 0 | 0 | 0 | -2.16 | 0.25 | 1.03 | 2.16 | 0.25 | 1.03
2. | 0 | 0 | 100 | -0.31 | 1.16 | 101.04 | 0.31 | 1.16 | 1.04
3. | 20 | 80 | 0 | 12.97 | 81.67 | -1.90 | 7.03 | 1.67 | 1.90
4. | 0 | 60 | 40 | -3.02 | 36.32 | 65.39 | 3.02 | 23.68 | 25.39
5. | 80 | 0 | 20 | 65.55 | -6.96 | 14.65 | 14.45 | 6.96 | 5.35
6. | 40 | 40 | 20 | 39.18 | 38.59 | 21.16 | 0.82 | 1.41 | 1.16
7. | 33.3 | 33.3 | 33.3 | 33.05 | 30.17 | 31.76 | 0.25 | 3.13 | 1.54
8. | 20 | 0 | 0 | 18.76 | 0.19 | -0.22 | 1.24 | 0.19 | 0.22
9. | 0 | 20 | 0 | 0.05 | 17.21 | -0.09 | 0.05 | 2.79 | 0.09
10. | 0 | 0 | 10 | 1.13 | -1.04 | 12.93 | 1.13 | 1.04 | 2.93
No | Absolute error |  |  | Sample Error
 | R | G | B | 
1 | 2.16 | 0.25 | 1.03 | 1.15
2 | 0.31 | 1.16 | 1.04 | 0.83
3 | 7.03 | 1.67 | 1.90 | 3.54
4 | 3.02 | 23.68 | 25.39 | 17.37
5 | 14.45 | 6.96 | 5.35 | 8.92
6 | 0.82 | 1.41 | 1.16 | 1.13
7 | 0.25 | 3.13 | 1.54 | 1.64
8 | 1.24 | 0.19 | 0.22 | 0.55
9 | 0.05 | 2.79 | 0.09 | 0.98
10 | 1.13 | 1.04 | 2.93 | 1.70
Mean Error |  |  |  | 3.78

## Slide 50: Model
No | Parameter | Nilai
1. | Number of neurons in the input layer | 15
2. | Number of hidden layers | 15
3. | Number of neurons in the output layer | 3
4. | Epoch | 300
5. | Learning rate | 0,001
6. | Normalization | No

## Slide 51: Result
No | Sample Concentration Content (%) |  |  |  |  |  |  |  | 
 | Actual |  |  | Prediction |  |  | Absolute error |  | 
 | R | G | B | R | G | B | R | G | B
1. | 0 | 0 | 0 | -4.17 | 3.46 | -0.30 | 4.17 | 3.46 | 0.30
2. | 0 | 0 | 100 | -4.44 | -0.22 | 96.55 | 4.44 | 0.22 | 3.45
3. | 20 | 80 | 0 | 18.98 | 83.83 | 1.31 | 1.02 | 3.83 | 1.31
4. | 0 | 60 | 40 | -10.98 | 21.52 | 68.48 | 10.98 | 38.48 | 28.48
5. | 80 | 0 | 20 | 76.70 | -0.70 | 17.75 | 3.30 | 0.70 | 2.25
6. | 40 | 40 | 20 | 40.71 | 40.92 | 21.41 | 0.71 | 0.92 | 1.41
7. | 33.3 | 33.3 | 33.3 | 26.52 | 19.19 | 40.35 | 6.78 | 14.11 | 7.05
8. | 20 | 0 | 0 | 14.65 | 0.47 | 0.53 | 5.35 | 0.47 | 0.53
9. | 0 | 20 | 0 | -0.03 | 16.22 | -1.54 | 0.03 | 3.78 | 1.54
10. | 0 | 0 | 10 | -3.08 | 0.65 | 11.48 | 3.08 | 0.65 | 1.48
No | Absolute error |  |  | Sample Error
 | R | G | B | 
1 | 4.17 | 3.46 | 0.30 | 2.64
2 | 4.44 | 0.22 | 3.45 | 2.70
3 | 1.02 | 3.83 | 1.31 | 2.05
4 | 10.98 | 38.48 | 28.48 | 25.98
5 | 3.30 | 0.70 | 2.25 | 2.08
6 | 0.71 | 0.92 | 1.41 | 1.01
7 | 6.78 | 14.11 | 7.05 | 9.32
8 | 5.35 | 0.47 | 0.53 | 2.12
9 | 0.03 | 3.78 | 1.54 | 1.78
10 | 3.08 | 0.65 | 1.48 | 1.74
Mean Error |  |  |  | 5.14

## Slide 52: Conclusion
Already able to get data from the prototype that was made
The data obtained from food colorant have appropriate values ​​between the concentration and the graphic form of the single red and green dyes. Meanwhile, for the blue dye and the mixed dye, the data obtained is still not in accordance with the graphic form, which has a difference with the number of concentration settings.
The first model with a simple layer architecture and using normalization has better predictive results than the model with a complex layer architecture with an error value of 3.78 compared to 5.14.

## Slide 53: Thankyou